4332K MOBILE DESK

ASSEMBLY INSTRUCTIONS

*Model views may not represent exact model purchased

TABLE OF CONTENTS

PAGE

REVISIONS TABLE…………………………………………………………………………………………………………………….…………………..……….…………..……….…………………………………...………..……………………………3

ASSEMBLY COMPONENTS…………………………………………………………………………………………………………………….…………………..……….……….……………...…………………………………………3

CASTER ASSEMBLY…………………………………………………………………………………….…………………..……….……………………………..……….…………………………………….……………………………………………4

ROD SOCKET ASSEMBLY…………………………………………………………………………………………………………………….…………………..……….…..………..………….………………………..……………………5

ROCKET PUMP ASSEMBLY…………………………………………………………………………………………………………………….…………………..……….…..….…….………………...…………………………………6

DRAIN ASSEMBLIES…………………………………………………………………………………………………………………….…………………..……….…..……….……………….………………………....…………………………………6

PULL ASSEMBLY…………………………………………………………………………………………………………………….…………………..……….…..……….…………….……………………..………………..………………………….………6

ASSEMBLY COMPONENTS

| ITEMS INCLUDED | PART # |  | PART # |
| --- | --- | --- | --- |
| ASSEMBLY INSTRUCTIONS |  | 1-HARDWARE BOX |  |
| 4-CASTERS, 4" SWIVEL PLATE | 100081 | 2-UPRIGHT RODS, 3/4 DIA X 36" L | 100004 |
| 1-CASTER HARDWARE BAG | 206509 | 1-CROSSBAR, 1/2 DIA X 40" L | 100007 |
| 2-1/2X3/4 ROD CLAMP W/THUMB SCREW | 100003/100490 | 2-WATER JUG, 2 1/2 GAL. | 100118 |
| 1-ELECTRICAL EXTENSION CORD | 100036 | 1-PEGBOARD, 20.5X26.885 | 206542 |
| 1-ROCKET HAND PUMP, RP800 | 100013 | 3.2FT FILE HANGER, PLASTIC | 100184 |
| 2.5FT TUBING, 3/8 FOR HAND PUMP | 100015 | 3-PEG HOOK, ASSORTED J-HOOKS | 100140 |
| 1-PEG HOOK, DBL STRAIGHT HOOK | 100113 | 2-PEG HOOK, SINGLE STRAIGHT | 100119 |

| A | Added Information for Troubleshooting GFCI Receptacle | 8/6/10 | DK |
| --- | --- | --- | --- |

REV	                                                 DESCRIPTION			                  DATE      INITIAL

| --- | Original Created | 5-13-09 | NAM |
| --- | --- | --- | --- |
| A | Added Information for Troubleshooting GFCI Receptacle | 8/6/10 | DK |

# Assembly Instructions for

4332K MOBILE DESK

WITH CAMERA STORAGE

Items not included but needed for assembly:

- ½” Wrench

- Adjustable pliers

Instructions:

- Attach the (4) 100081 4” Swivel Top Plate, W/Brake Casters into place using the (16) 100488 Screw, ¼” - 20X1 ¼” slotted flat, (16) 218589 Washer, ¼” Flat, Zinc Plated & the (16) 100483 Nut, ¼” - 20 Hex Zinc into the bottom of the base as shown.

Figure 1

Figure 1A Detail

- Assemble the Rod Socket Assembly as shown in Figure 9A.

Attach Rod Sockets to Top as shown in Figure 9B.

Figure 9A

Figure 9B

- Attach the Rocket Pump to the top using the (2) screws provided with the unit.

- Attach 3/8” tubing (100015) from the bottom of the Rocket Pump (100013) into a 2.5 gallon water jug (100118) as shown.  Attach 1-1/2” drain tube from sink into the second 2.5 gallon water jug (100118)

NOTE: Side panel removed for display purposes only.

- Reverse Pulls to Exterior of unit as shown.

- Clean top with water only.

TROUBLESHOOTING YOUR GFCI ELECTRICAL RECEPTACLE:

PLEASE NOTE: THROUGHOUT ANY OF THE FOLLOWING STEPS (PROCEDURES); IF YOU ARE NOT SURE YOU CAN DO THIS JOB SAFELY, AND COMPETENTLY, REFER THIS WORK TO QUALIFIED PROFESSIONAL!

If your unit comes equipped with a GFCI (Ground Fault Cicruit Interrupter) electrical receptacle, and there is no power in the receptacle please consider/check the following:

- The extension cord (if being used) is working properly.

- The breaker hasn’t been tripped, or turned off.

This type of GFCI has two testing-related buttons on it. One button is appropriately labeled “TEST”, and the other button is labeled “RESET”. To test the GFCI receptacle follow these steps:

- Plug in an appliance (lamp or night light) into the outlet.   The light should now be on.  Then press the “TEST” button on the GFCI.  The GFCI “RESET” button should pop out, and the light should go out.

- If the “RESET” button pops out, but the light doesn’t go out, the GFCI has been improperly wired.  In this case please contact a certified professional.  There may also be a problem with other wiring in the same circuit.

- If the “RESET” button doesn’t pop out, the GFCI is defective, or malfunctioned, and should be replaced.

- If the GFCI is functioning properly, and the lamp goes out, press the “RESET” button to restore power to the outlet.

Conversely, if you have a GFI that has tripped (which is common) and it will not reset, you may have a wiring short in the circuit, a defective appliance on the circuit, or the GFI itself has become defective.  To test a tripping GFCI follow these steps:

- Remove every appliance connected to the GFCI's circuit and reset it. If it doesn't reset there may either be a wiring fault behind a socket outlet, or your GFCI itself has become faulty.

- Make sure whatever you are plugging into to the GFCI is dry and not damaged.

- Only plug in one item at a time. If you are plugging in a defective item it will cause the GFCI to trip, and that item therefore should be replaced.

If you are still having difficulty the easiest way to troubleshoot a GFI is to obtain a GFI tester, which is available at most hardware stores.  It plugs into the GFI outlet, and will supply you with a "snapshot" of your connections, indicating wiring problems and/or the condition of the GFI.  Another way to troubleshoot is to simply purchase a new GFI and install it.